## Slide 1
Biomaterials Module:
Review
Collin Schmidt, M.S.
December 3rd, 2025

## Slide 2: Module Review
Potential exam questions
L1 – Introduction to Biomaterials
L2 – Biocompatibility
L3 – Metals
L4 – Metals + Ceramics
L5 – Polymers

## Slide 3: Immune Response
What are the stages of immune response?
Why is it important to be familiar with these stages? How do we apply this knowledge to change our engineered response?
How do we determine if a material generates an immune response? What cell types are involved in an immune response?
Some patients’ immune responses can take weeks to present? Why is that so?
Carnicer-Lombarte A, Chen ST, Malliaras GG, Barone DG. Foreign Body Reaction to Implanted Biomaterials and Its Impact in Nerve Neuroprosthetics. Front Bioeng Biotechnol. 2021;9. doi:10.3389/fbioe.2021.622524

## Slide 4: Crystal Lattice
Why is it important to understand how a material forms a crystal lattice?
  What are some applications as engineers?
What are the three main types of crystal lattices discussed in this class?
How do the densities compare between the crystal lattices?
Which class(es) of materials typically present themselves in a crystal lattice?
Provide an example of a material for each crystal lattice (at room temperature)?
How can the unit cell be modified to change material properties?
Veritasium. (2025, November 17). *Why don’t jet engines melt?* [Video]. YouTube. [https://www.youtube.com/watch?v=QtxVdC7pBQM](https://www.youtube.com/watch?v=QtxVdC7pBQM) ([youtube.com][1])
Notes: https://www.youtube.com/watch?v=QtxVdC7pBQM
Veritasium. (2025, November 17). *Why don’t jet engines melt?* [Video]. YouTube. [https://www.youtube.com/watch?v=QtxVdC7pBQM](https://www.youtube.com/watch?v=QtxVdC7pBQM) ([youtube.com][1])
[1]: https://www.youtube.com/watch?v=QtxVdC7pBQM&utm_source=chatgpt.com "What happens if you throw sand into a jet engine?"

## Slide 5: Design a prosthetic limb
Design a prosthetic from what you know about biomechanics and bioinstrumentation
  Tie in concepts from each module
  Explain your material choices
  Consider interaction of materials
    i.e. metal-on-metal corrosion
Metal
(ceramic surface mod)
Polymer
(UHMWPE)
Metal
(Ti Alloy)
Ceramic

## Slide 6: Stress-Strain Curves
Modulus of Elasticity – slope of linear region of stress-strain curve
Yield Strength – intersection of stress-strain curve with 0.2% offset strain
Ultimate tensile strength – max stress on stress-strain curve
Fracture strength – stress at which failure occurs
Ductility – strain at which failure occurs (reported in %)
Notes: Modulus = 400 MPa/0.008 = 50 Gpa
Yield Strength
UTS
Ductility

## Slide 7: Stress-Strain Curves
Biomaterial | Conductivity | Ductility (Fracture Toughness) | Modulus of Elasticity | Ultimate Tensile Strength
Metal | High | Med | High | High
Ceramic | Low | Low (Brittle) | High | High
Polymer | Med (some are conductive) | High | Low | Low

## Slide 8: Module Objective
Understand factors important to the design and selection of biomaterials
Focus Areas:
Structure-property relationships
Biocompatibility/Host response
Types of biomaterials
Selection & Example Applications

## Slide 9: Module Review
Potential exam questions
L1 – Introduction to Biomaterials
L2 – Biocompatibility
L3 – Metals
L4 – Metals + Ceramics
L5 – Polymers

## Slide 10: Biomaterials Definitions
Old Definitions:
1. A non-viable material used in a medical device, not intended to interact with biological systems
Williams DF, 1987
2. A synthetic material used to replace part of a living system or to function in intimate contact with living tissue
Park JB +, 1992

## Slide 11: Current Biomaterials Definition
A biomaterial is a viable or non-viable material that interacts with the biological environment, and its function is to diagnose, treat, support, augment or replace part or all of a living system
  Functional
  Biocompatible (performs specific function with an appropriate host response)
  Non-carcinogenic
  Non-toxic
  Long term stability

## Slide 12: Clinical Need for Biomaterials
Biological Grafts
  Autograft – graft from self
  Allograft – graft from other, same species
  Xenograft – graft from other, different species
  Which is preferred? Why? Which is more commonly used? Why?
  Autografts  Elicit little to no immune response
  Allografts and xenografts are easier to obtain  Autograft supply does not meet demand
Notes: Also donor site morbidity  Tissue engineering as a solution to grafting

## Slide 13: Biocompatibility
Biocompatibility is the ability of a material to perform with an appropriate host response in a specific application
Williams, 1987
  Inflammation
  Wound Healing Response (expected)
  Allergic Response (should not induce)
  Infection (should not induce)
  YES, inflammation is an appropriate host response to a foreign body, should not provoke chronic inflammation
  Is an implant that causes acute inflammation biocompatible?

## Slide 14: Definitions for study sheet
Notes: More than just tolerable  Bioactive, immune modulation, tissue engineering

## Slide 15: More Definitions...
Notes: Biocompatibility mainly has to do with the host response – how does the body interact with the material?
Biofunctionality focuses on the material response – how does the material respond in the host environment?
Very dynamic

## Slide 16: Wound Healing: Inflammation
Initial Events
  Coagulation factor XII is activated when in contact with foreign proteins/material
  Fibrous clot forms (platelets aggregate)
    Purpose  1) Localizes the inflammatory response, 2) prevent blood loss
  Local capillaries dilate and the permeability of the vessel endothelium increases
  Increased blood flow to the region, allows chemotaxis of immune cells
Image source: Janeway’s Immunobiology, 9th ed.
HW2 Q1A

## Slide 17: Wound Healing Summary
AVOID going into chronic healing, granulation tissue (fibrous capsule)
HW2 1b:
Fibrous capsules contribute to atrophy by limiting nutrient and blood supply

## Slide 18: Wound Healing Summary
Fibrous encapsulation (end of inflammation response):
dense, acellular, avascular collagen network

## Slide 19: Types of Biomaterials
Metals
Polymers
Ceramics
Glasses
Natural materials
Composites
  Things to know 
  When it is appropriate to select which type
  An example for each
  Advantages & Disadvantages

## Slide 20: Structure-Property Relationships
DeBeers Diamond
428.5 Carats
100% C
Graphite Pencil Lead
100% C
Crystal Structure – Diamond’s crystal lattice is more organized, more tightly packed than graphite’s
Bond type determines material properties
Same material composition – What causes the differences in properties?
Notes: These are not biomaterials! Merely an example of how crystal structure and interatomic bonding can confer vastly different material properties. When thinking about a metal, ceramic or polymer you should be think from this atomic scale to the macroscale in terms of how this material will interact with the body. And that’s the key here, for instance on the homework there was a question about the types of bonds and give a biomaterial example, it is insufficient to say metal when you should say titanium used for hip implant, or calcium phosphate ceramic pastes used as bone filler or surgical bone cement the specific material and the application are both critical
What is always the driving force for bonding and what are the bond types?
Graphite possesses a giant covalent structure with only carbon atoms forming hexagonal rings, no ionic bonding present. Also it might help to remember that ionic compounds do not conduct electricity in solid state as the ions are not free to move like metallic bonds are, but graphite is extremely conductive and actually work in the Lu Lab uses electroactivity of graphite to stimulate chondrocytes to make cartilage, this should help you remember that graphite must not be an example of ionic bonding

## Slide 21: Interatomic Bonding
Metal – metallic bonding, non-directional
Ceramic – ionic or covalent bonding
Polymer – covalent bonding, secondary bonding, directional
Notes: METALS: metallic bonding is the reason why metals are malleable, i.e. ductile because the atoms can so easily roll past eachother under applied load due to this free electron sharing, ALSO by allowing free electrons to move between the atoms metals are extremely conductive . ... Since like charges repel each other, the movement of one free electron within the lattice dislodges those in the next atom, and the process repeats – moving in the direction of the current, toward the positively charged end
CERAMICS: Ionic (predominant) strong electrostatic attraction forces formed between positive and negative ions, between a metal & nonmetal according to the electronegativity of the element in the bond. Electronegativity is the capability of the nucleus in an atom to attract and retain all the electrons within the atom itself, and depends on the number of electrons and the distance of the electrons in the outer shells from the nucleus.. This bond is non-directional, meaning that the pull of the electrons does not favor one atom over another;
Can also be covalent which is directional bonding between nonmetals (similar electronegativities), like carbon atoms, where the electrons are shared
Ionic example should clarify ceramic bone screws where ionic bonds are present or if bone plates and screws are metals there is ionic bonding between the metal (or metal oxide layer) and the bone tissue itself.
POLYMERS: there are covalent bonds between the atoms of the polymer, but the polymeric macromolecules (or chains) are kept together by Van der Waals forces. Of all the four types of bonds, Van der Waals is the weakest. For this reason, polymers are very elastic (e.g., a rubber band), can be easily melted, and have low strength

## Slide 22: Interatomic Bonds
Driving force for bond formation: lower energy state
Primary
  Ionic (600-1500 kJ/mol)  Non-directional
  Covalent (50-200 kJ/mol)  Directional
  Metallic (68-850 kJ/mol)  Non-directional
Secondary
  Van der Waals (~20 kJ/mol)
  Hydrogen bonding (51 kJ/mol)
Notes: the number of kilojoules of energy that it would take to break apart exactly one mole of those bonds
ionic bonds are formed through electrostatic attraction
between oppositely charged ions, and metallic bonds are composed of a sea of valence electrons that can
flow through the entire metal in any direction. This means that the magnitude of nondirectional bonds is
equal in all directions around the atom/ion and there are fewer restrictions on the orientation of
neighboring atoms/ions. Covalent bonds, on the other hand, are directional. They are formed by the
sharing of electrons between two atoms, so covalent molecules have a definite shape because specific
atomic orientations are preferred. As a result, the atoms are stuck in specific configurations and generally
can’t pack together as densely as nondirectionally bonded materials.

## Slide 23: Property Charts  Study Sheet
Notes: Also in L1 for electrical conductivity, density, and other mechanical properties

## Slide 24: Surface vs. Bulk Properties
Surface Properties
  Electrolyte-material interactions
    CORROSION
  Cell-material interactions
    Determined by surface texture
  Protein adhesion and conformation
    Race to the surface, want a non-fouling surface to prevent implant rejection
Bulk Properties
  Mechanical, electrical, and optical
Why do surface properties differ from bulk?
Atoms in bulk are bound to surrounding unit cells, surface atoms are more reactive

## Slide 25: Lecture Summary

## Slide 26: Module Review
Potential exam questions
L1 – Introduction to Biomaterials
L2 – Biocompatibility
L3 – Metals
L4 – Metals + Ceramics
L5 – Polymers

## Slide 27: Crystal Lattice Structures
Face centered cubic (FCC)
Body centered cubic (BCC)
Hexagonal close packed (HCP)
Notes: Question 3a on the hw

## Slide 28: Important equations
Theoretical Density
Atomic Packing Factor

## Slide 29: FCC  Study Sheet

## Slide 30: BCC  Study Sheet

## Slide 31: HCP  Study Sheet

## Slide 32: Iron Exists in Two Forms (Polymorphism)
Austenite (FCC) form of iron is stronger than α ferrite (BCC) form
α ferrite at room temperature, austenite at higher temperatures
Adding Cr will oxidize, but preserve α ferrite form
Stabilize austenite form by doping the lattice with Ni
Notes: Ni is FCC

## Slide 33: Packing structures
ASTM F136 Titanium Alloy consists of a FCC and/or HCP unit cell geometry
ANSI 316L Stainless Steel alloys exhibit an FCC and/or BCC unit cell geometry
Notes: Remember these!

## Slide 34: Metal examples: AISI 316L (Stainless Steel)
AISI 316L |  | 
Fe | 60-65% | 
Cr | 17-19% | Forms Cr2O3 to passivate the stainless steel surface
Ni | 12-14% | Stabilizes the austenite (FCC) form of iron which is stronger than α ferrite (BCC), forms substantial defects in the iron structure Increases corrosion resistance
C | <0.03% | Form interstitial defects which increase resistance to deformation or plane slip REDUCES corrosion resistance
Mo | 2-4% | Competitively binds to Cl- to prevent pitting corrosion of steel and reduce corrosion in physiological fluids
Mg | 2% | Processing agent
Trace elements: Cu N, P, Si, S, Mn |  | 
Notes: When strengthening a material, you want the crystal size to increase and grain size to decrease

## Slide 35: Metal examples: AISI 316L (Stainless Steel)
(+) Strength
(+) Ease in manufacture and molding into desired shapes
(+) More economical compared to other metallic biomaterials
(-) Corrosive in vivo
(-) Strength mismatch: stress shielding
Notes:
Pros/Cons:
Applications:
Orthopedics & Cardiovascular (stents)

## Slide 36: Metal examples: Cobalt-Chromium (Co-Cr-Mo) Alloys
(+) Better fatigue strength than AISI 316L
(+) Good for applications with long service life
(+) Improved corrosion resistance under stress
(-) Poor wear properties, toxic wear products
(-) Stress shielding, corrosive in vivo
Notes:
Pros/Cons:
Applications:
Orthopedics

## Slide 37: Metal examples: Ti and Ti Alloys
(+) Lightweight compared to other metals
(+) Greater strength/density than other metals
(+) Improved corrosion resistance (surface oxide layer – TiO2), improved biocompatibility
(-) Stress shielding, poor shear strength (can’t use as screws/plates)
(-) Corrosive in vivo, expensive
Notes:
Pros/Cons:
Applications:
Orthopedics & Dental
Make sure you know what all the elements in the alloys do!

## Slide 38: Fabrication and Strengthening
Fabrication/Surface Modification Methods:
  Casting
  Solid State Sintering
Strengthening Methods
  Solid Solution Hardening
  Plastic Forming and Annealing
  Hot Isostatic Pressing
  Precipitation Hardening

## Slide 39: Fabrication Methods

## Slide 40: Processing Methods
Plastically deforming a metal at a certain temperature will alter grain strucutre -> confers mechanical properties
Annealling  heat metal & cool slowly controlled rate to remove internal stresses and toughen
Notes: Annealling  Reduces dislocations , allows atoms to move and reorganize , upon cooling they stabilize in structure with lower energy increase toughness, reduce hardness, increase ductility larger grain size, increase grain boundary lower SA to vol ratio
Hot working increases ductility  Defect free grains! Heat to recrystallization temp but below melting temp allows grains to form without residual stress
Cold working decreases ductilitly strengthens metal, introduces defects reduce movement of crystals  stronger
Smaller grains have greater SA to vol ratio more grain boundaries to dislocations  harder material

## Slide 41: Processing Methods
Notes: Produces smaller grain size  strengthens

## Slide 42: Processing Methods
Notes: Dissolving precipitates and reducing segregation might be present in alloy  becomes homogenous
Quench make solid rapidly in order to prevent precipitate formation
Precipitates form in finely dispersed manner
Preciptates are clusters of impurity defects (i.e. alloying material)

## Slide 43: Corrosion
EMF series (+ is less reactive)
Nernst equation
Notes: Emf series positive value won’t corrode, neg value highly reactive

## Slide 44: Metals Summary

## Slide 45: Module Review
L1 – Introduction to Biomaterials
L2 – Biocompatibility
L3 – Metals
L4 – Metals + Ceramics
L5 – Polymers
Potential exam questions

## Slide 46: Ceramics

## Slide 47: Bioinert Ceramics
Alumina
Zirconia
Notes: There are three types of ceramics: bioinert, bioactive, and bio resorbable. For the first type, Helen gave two examples.

## Slide 48: Bioactive Ceramics
Elicit a specific biological response which results in biological bonding
  Formation of carbonated hydroxyapatite layer at tissue-material interface
  Bioactive glasses

## Slide 49: Bioresorbable Ceramics
Degrade gradually and allow for replacement by host tissue
  Calcium phosphate ceramics
    Tricalcium phosphate
      Ca3(PO4)2
      Ca/P = 1.50
    Hydroxyapatite
      Ca10(PO4)6(OH)2
      Ca/P = 1.67
      Mech properties from homework

## Slide 50: Definitions for Study Sheet
Osteointegration
  Chemical integration between bone and implant (Ex: bioactive glass)
Osteoconduction
  Materials that provide a scaffold for bone-forming cells and subsequent bone formation
  Interconnecting porosity for cell and vascular growth (Ex: Hydroxyapatite)
Osteoinduction
  Materials that have a capacity to induce bone (recruit stem cells, induce proliferation/differentiation)
  Ex: Demineralized bone matrix

## Slide 51: Ceramics Summary

## Slide 52: Ceramics Summary

## Slide 53: Module Review
L1 – Introduction to Biomaterials
L2 – Biocompatibility
L3 – Metals
L4 – Metals + Ceramics
L5 – Polymers
Potential exam questions

## Slide 54: Homopolymers and Copolymers
Copolymer

## Slide 55: Homopolymers and Copolymers

## Slide 56: Definitions for Study Sheet

## Slide 57: Example polymers: Polyethylene

## Slide 58: Example polymers: PMMA

## Slide 59: Example polymers: Polyesters

## Slide 60: Degradable Polymers in Medicine
Can tailor drug release by controlling PLA:PGA ratio
  PGA is more hydrophilic, degrades faster whereas PLA has a methyl group that prevents water infiltration (shields ester bonds), degrades slower
Know the name and structure of at least one SPECIFIC polymer for surface and bulk erosion

## Slide 61: PLA + PGA = PLGA
100% PGA gives half life of 5 months
100% PLA gives half life of > 6 months
50/50 PGA/PLA gives half life of several weeks
A.
B.
C.
PGA only  bulk eroding
PLA only  bulk eroding, but has a methyl group to hinder water infiltration
50/50 PGA/PLA Intermingling of polymer chains, less crystalline lattice, more water infiltration, degrades the fastest
Notes: PLA has a methyl group, slows hydrolytic degradation. PGA and PLA have mismatch in packing, mixing them decreases the crystallinity

## Slide 62: Degradable Polymers in Medicine
Surface Eroding Polymers
  Rate of water infiltration < Rate of hydrolysis
    Hydrophobic polymers
  Degradation limited to the surface
  Device becomes thinner over time
  Maintains structural integrity
  Ex: Polyanhydrides, PCL
Bulk Eroding Polymers
  Rate of water infiltration > Rate of hydrolysis
    Hydrophilic Polymers
  Pockets of eroded polymer – burst release
  Ex: Polyesters, sugar cube, PLA/PGA/PLGA

## Slide 63: Polymer Summary

## Slide 64: Module Review
L1 – Introduction to Biomaterials
L2 – Biocompatibility
L3 – Metals
L4 – Metals + Ceramics
L5 – Polymers
Potential exam questions

## Slide 65: Immune Response
What are the stages of immune response?
Why is it important to be familiar with these stages? How do we apply this knowledge to change our engineered response?
How do we determine if a material generates an immune response? What cell types are primarily implicated in an immune response?
Some patients’ immune responses can take weeks to present? Why is that so?
Carnicer-Lombarte A, Chen ST, Malliaras GG, Barone DG. Foreign Body Reaction to Implanted Biomaterials and Its Impact in Nerve Neuroprosthetics. Front Bioeng Biotechnol. 2021;9. doi:10.3389/fbioe.2021.622524

## Slide 66: Crystal Lattice
Why is it important to understand how a material forms a crystal lattice?
  What are some applications as engineers?
What are the three main types of crystal lattices discussed in this class?
How do the densities compare between the crystal lattices?
Which class(es) of materials typically present themselves in a crystal lattice?
Provide an example of a material for each crystal lattice (at room temperature)?
How can the unit cell be modified to change material properties?
Veritasium. (2025, November 17). *Why don’t jet engines melt?* [Video]. YouTube. [https://www.youtube.com/watch?v=QtxVdC7pBQM](https://www.youtube.com/watch?v=QtxVdC7pBQM) ([youtube.com][1])
Notes: https://www.youtube.com/watch?v=QtxVdC7pBQM
BCC – Cr
FCC – Al
HCP - Mg

## Slide 67: Design a prosthetic limb
Design a prosthetic from what you know about biomechanics and bioinstrumentation
  Tie in concepts from each module
  Explain your material choices
  Consider interaction of materials
    i.e. metal-on-metal corrosion
Metal
(ceramic surface mod)
Polymer
(UHMWPE)
Metal
(Ti Alloy)
Ceramic

## Slide 68: Stress-Strain Curves
Modulus of Elasticity – slope of linear region of stress-strain curve
Yield Strength – intersection of stress-strain curve with 0.2% offset strain
Ultimate tensile strength – max stress on stress-strain curve
Fracture strength – stress at which failure occurs
Ductility – strain at which failure occurs (reported in %)
Notes: Modulus = 400 MPa/0.008 = 50 Gpa
Yield Strength
UTS
Ductility

## Slide 69: Stress-Strain Curves
Biomaterial | Conductivity | Ductility (Fracture Toughness) | Modulus of Elasticity | Ultimate Tensile Strength
Metal | High | Med | High | High
Ceramic | Low | Low (Brittle) | High | High
Polymer | Med (some are conductive) | High | Low | Low

## Slide 70: Thank You!
Good luck!

## Slide 71: Characteristics of Inflammation

## Slide 72: Factors Controlling Capsule Thickness

## Slide 73: Corrosion Prevention

## Slide 74: Module Review
L1 – Introduction to Biomaterials
L2 – Biocompatibility
L3 – Metals
L4 – Metals + Ceramics
L5 – Polymers
L6 – Current Trends in Biomaterials
Potential exam questions

## Slide 75: Biomaterials in the Hip

## Slide 76: Factors Controlling Degradation
Starting Polymer:
Crystallinity (higher, slows degradation)
  Crystalline – densely packed chains
  Amorphous/glassy – higher backbone hydrolysis
  Amorphous/rubbery – increased permeability to water
Molecular Weight (Higher, slows degradation)
Surface Energy (Hydrophilic/phobic)
Backbone Chemical Stability (Anhydride bonds hydrolyze faster than ester, which hydrolyze faster than amide
Degree of Crosslinking
  Can interfere with crystal lattice and speed bulk degradation OR strengthen matrix and slow degradation

## Slide 77: Natural/Biological Materials Summary

## Slide 78: Strain fracture toughness
Critical Stress
Strain Fracture Toughness
Initial stress v strain curve prior to fracture
Calculate the strain fracture toughness KIC for a material, given the specific surface energy (s)
Notes: 5) Convert to SI Units
J = N*m  J/m2 = N*m/m2 = N/m
(Pa*J/m2)1/2 = [(N/m2)*(N/m)]1/2=(N2/m3)1/2=(N2/m4 * m)1/2=N/m2*(m)1/2=Pa*m1/2